Jim Rosemary (rosemary@eecis.udel.edu)

This code was taken from a terminal emulator that I wrote a while
back. The entire program was written in machine language and each
revision was burned into an EPROM for the target system. Because of
this, I did not try to make the code too 'pretty' - I just wanted to
get it running. Read at your own risk.

Also, be advised that not all keyboards work with my machine. The better
of the two keyboards that I have tried works fine, whereas the cheap one
will not work at all.

It is advisable to obtain the keyboard docs from ftp.ee.ualberta.ca
in the /pub/cookbook directory and read them.

A 6522 is mapped at $fe30
PB0 goes to DATA
PB1 goes to CLOCK
Also, one of the control lines (CB1 or CB2, whichever corresponds
to Interrupt enable $10)

No interrupt code is provided here; only the actual transfer.

$ff is used for passing data to/from the Get Byte and Write Byte routines.
Reset has no parameters.

Get Byte:

		lda $fe32
		and #fc
		sta $fe32
		jsr get_bit
		ldy #$09
loop:		jsr get_bit
		ror $ff
		dey
		bne loop
		jsr get_bit
		lda $ff
		rts

get_bit:
		lda #$02
wait_for_hi	bit $fe30
		bne wait_for_hi
		lda $fe30
		pha
		lda #$02
wait_for_low	bit $fe30
		bne wait_for_low	
		pla
		lsr
		rts

Write Byte:
		lda $fe30
		and #$fc
		sta $fe30
		lda $fe32
		ora #03
		sta $fe32
		ldx #$c0
wait:		dex
		bne wait	
		lda $fe32		// Write start bit
		and #$fd
		sta $fe32
		lda #$02
wait_for_hi	bit $fe30		// Wait for clock line
		beq wait_for_hi
wait_for_lo	bit $fe30
		bne wait_for_lo	
		ldx #$08
		lda $fe32
		ldy #$01
loop		lsr $ff
		jsr write_bit		// Write data bits
		dex
		bne loop
		tya
		lsr			// Write parity
		jsr write_bit
		sec			// Write stop bit
		jsr write_bit
		lda #$01
wait_lo		bit $fe30		// Wait for handshake from kbd
		bne wait_lo
		rts

write_bit
		lda $fe32
		and #$fe
		bcs write_one
		ora #$01
		iny
write_one	sta $fe32
		lda #$02
wait_for_lo	bit $fe30
		bne wait_for_lo
wait_for_hi	bit $fe30
		beq wait_for_hi 
		rts

Reset Keyboard:
		lda $fe30
		and #$fc
		sta $fe30
		lda $fe32
		ora #$03
		sta $fe32
		ldx #$c0
wait		dex
		bne wait
		lda $fe32
		and #$fd
		sta $fe32
		lda #$02
wait_for_hi	bit $fe30
		beq wait_for_hi
wait_for_lo	bit $fe30
		bne wait_for_lo
		ldx #$08
		lda $fe32
		and #$fe
		sta $fe32
		lda #$02
wait_for_hi1	bit $fe30
		beq wait_for_hi1
wait_for_lo1	bit $fe30
		bne wait_for_lo1
		dex
		bne wait_for_hi1 
		lda #$02
wait_for_hi2	bit $fe30
		beq wait_for_hi2
wait_for_lo2	bit $fe30
		beq wait_for_lo2
		lda #$01
wait_for_lo3	bit $fe30
		bne wait_for_lo3
		lda #$10
		sta $fe3d
		rts